## Slide 1: Measures to Support Safety in Dental Radiography in the Digital Age
Pamela Alston, DDS, MPP
Lead Oral Health Specialist

## Slide 2: Participants will be able to:
Describe dental radiation risks
Review the proper safety measures for dental x-ray equipment operators
Explain the safety measures necessary for the protection of the students when dental x-rays are taken.

## Slide 3: Radiation Physics
Energy—ability to do work
Matter—occupies space & has form
Matter—composed of atoms
Molecule—smallest particle

## Slide 4: X-rays
Form of energy penetrating matter
Classified as electromagnetic radiation traveling through space with a wavelike motion
Shorter the wavelength, greater the energy

## Slide 5: Radiation Effects
All ionizing radiation is harmful
Produces biologic changes in living tissues
Entire x-ray area is a radiation hazard area

## Slide 6: Electromagnetic Radiation

## Slide 7: Tissue Damage
Patient’s tissues absorb some X-rays

## Slide 8: X-ray Tubehead can leak radiation

## Slide 9: Biologic Effects
Affects body chemicals, cells, tissues & organs
Effects may not become evident for years
Time lag is called latent period

## Slide 10: Cumulative Effects
Repeated exposure damages tissue
Some repair occurs
Tissues do not return to original state

## Slide 11: Acute & Chronic Radiation Exposure
Acute—large dose absorbed in short time
Chronic—small doses absorbed repeatedly over long period

## Slide 12: Genetic & Somatic Effects

## Slide 13: Critical Organs
ARPANSA.gov.au

## Slide 14: Selective risks from radiation sickness

## Slide 15: Radiation Units
Roentgen: a unit for measuring the amount of gamma or X-rays in air
Rad: a unit for measuring absorbed energy from radiation
Rem: a unit for measuring biological damage from radiation

## Slide 16: Maximum Permissible Dose
Reference: The University of Iowa Environmental Health & Safety
Maximum accumulated lifetime dose calculation:
(N-18) x 5 rems/year or (N-18) x 0.05 Sv/year
In this formula, N is the operator’s age.

## Slide 17: PRH-6.10, R2(c)
An elective oral examination, including bitewing x-rays…
shall be completed…

## Slide 18: Radiation Safety
I’ve heard x-rays are bad for me. Do you really have to take them?

## Slide 19: Patient Education
“Dental manufacturers are continually striving to develop products.”
“Digital radiography requires much less radiation than conventional radiography.”
“With less radiation, the absorbed dose to the patient is significantly lower.”

## Slide 20: Digital Radiography

## Slide 21: The dentist has responsibilities for dental imaging
Prescribe only images that are required for dx purposes
Ensure radiographic equipment is safe
Ensure appropriate shielding
Require that all personnel are properly trained & supervised
Use techniques that will produce diagnostic-quality images
Follow the state’s radiographic licensing requirements
Participate in obtaining informed consent

## Slide 22: ALARA Concept
All exposure to radiation must be kept to a minimum or “as low as reasonably achievable.”

## Slide 23: Protective Devices
Aluminum filtration
Collimator
Position indicator device
Lead apron and thyroid collar

## Slide 24: Lead Apron & Thyroid Collar

## Slide 25: Protective Devices-continued
Fast-speed film
Image receptor-holding devices
Exposure factor
Proper technique

## Slide 26: Monitoring
Operator protection & monitoring
Radiation monitoring
Equipment monitoring

## Slide 27: Pregnancy
No need to alter radiographic procedures

## Slide 28: Infection Control
Potential for cross-contamination
Wear personal protective equipment
Use heat tolerant intraoral devices
Transport and handle exposed film aseptically
Consult manufacturer for disinfection/sterilization advice

## Slide 29
Major References: Bird DL, Ronbinson DS. Modern Dental Assisting, El Sevier Saunders Publisher (2012)
Jansen Howerton, Laura. Dental Radiation Health, Updated 1st Edition, Western Schools (2017)